Texter Write-up
Started: 03.15.2020
Written: 04.21.2020
Finished:
Author: Jonathan Jacobson

Chip: PIC18F45J10

Table of Contents:

Goal:

The goal of this project is to create a handheld, battery powered radio transmitter that sends text over the 433MHz band to other devices. The text to be sent is written to the device through a USB keyboard which attaches to the device.

Block Diagram and Description:

[USB Keyboard]
       ↓
[LCD] ← [PIC18F45J10] → [HC-12]

LCD outputs what has been typed into the keyboard and also what has been received by the transmitter.

Hardware and Reasoning for choosing:
PIC18F45J10: Had 2 on hand, has serial onboard already.
HC12: Transmits data serially over 433MHz band. Small form factor. 2 Pins – works on 3.3V
LCD: 16x2 – Has decent amount of text on screen, is small. Takes only 6 pins from PIC18F45J10.

Wiring Diagram:

Software:
Components by function:
LCD: LCD Driver
433MHz: Sends serial data
USB: Acts as USB host and gets keypress data

Structure of Main Loop:

checks if the device is receiving → if so put in input buffer

checks if there is anything in output buffer → if so transmit → output buffer

checks if in transmit mode → if stuff in edit buffer put to LCD after clearing→ checks if Keyboard has keypress → if so put in edit buffer and put to LCD→ if enter given, put edit in output buffer & clear LCD

checks if in receive mode → checks if input buffer has anything → if so put to LCD after clearing→ wait for enter to go to next msg, if at end clear LCD and input buffer

Testing:

transmitter and lcd tested with abc loop, works well
Final Abilities:

Future Upgrades and what might be needed to accomplish

encryption
built-in key
usb key that can be added
voice transmission
buzz certain device number
external anteanna
more powerful transmitter
external power source
rechargable battery
computer-to-device ability
device outputs received data to computer
computer acts as keyboard for device
different frequencies
smaller form factor

Files:
Wiring Diagram
PCB Diagram
Software
PIC18F45J10
Settings for other chips
3D models